## Slide 1: WEEK 3 Transistor Model - BJT
Dr. Aron Michael 2023
Electrical Engineering & Telecommunications
Engineering

## Slide 3: Learning Outcomes
At the end of this week, you will be able to
  Draw the small signal circuit model of BJT.
  Calculate the small signal circuit model parameters of BJT.
  Draw the small signal equivalent circuit of BJT based amplifiers.
  Analyze the performance of the amplifiers such as gain, bandwidth, input impedance and output impedance.
  Draw the DC equivalent circuit of BJT based amplifiers and calculate the quiescent values (ICQ, IEQ, IBQ, VCEQ ).
  Explain DC biasing configurations such as current mirrors.

## Slide 4: Transistor Circuit Model - BJT
The circuit model will consist of resistors, current controlled current or voltage sources and capacitors
The small signal variations are about a given operating quiescent-point or Q-point (IBQ, ICQ, VBEQ, VCEQ)

## Slide 5: Transistor Circuit Model - BJT

## Slide 6: Transistor Circuit Model - BJT
The variations in the base and collector currents can be written in the following form:
Now and are functions of two variables ( and ), we take a Taylor expansion of the function about the Q‐point and consider only the first‐order terms by assuming that the small signal inputs are small

## Slide 7: Transistor Circuit Model - BJT
The gm, gπ, go and gμ are parameters that we choose to define the differential conductance:
Determination of gm and gπ
  From BJT transistor in active mode, VBE and IC are related as follows

## Slide 8: Transistor Circuit Model - BJT
The base current, IB,
Assuming IS and β are constant, gm and gπ can be obtained by differentiating the above expressions w.r.t. vBE and evaluating at the Q‐point values.
at 300K

## Slide 9: Transistor Circuit Model - BJT
In the active region, iC‐vCE curves are not perfectly horizontal lines, but have finite slopes (as shown in the graph above).
This is caused by an effect known as Base‐Width Modulation (also referred as the Early effect).

## Slide 10: Transistor Circuit Model - BJT
How does Base-width Modulation work?
By increasing vCE, we are increasing the reverse‐bias voltage across the C‐B junction. The depletion region of this junction is thus increased, resulting in a decrease in the effective base width, W.
Since IS is inversely proportional to W, IS, and hence iC, will increase. This is base‐width modulation.

## Slide 11: Transistor Circuit Model - BJT
Determinations of go and gu
  By definition ,
  this is the slope of the iC(vCE) characteristic, given by the Early effect as:
  where VA is early voltage
A note on magnitudes: the g parameters are related as

## Slide 12: Transistor Circuit Model - BJT
Each of the conductance increments (go, gm, gu, gπ) is directly proportional to the quiescent collector current IC and are functions of temperature and collector voltage.
For β large and VT/VA < 1/β, typically:
If we neglect the effects of base‐width modulation [i.e., VA = –∞],
Example: Given an npn transistor β = 40, IC = 2mA, VA = ‐ 65 volts
  gm = 80 mΩ‐1 gπ = 2 mΩ‐1
  go = 0.031 mΩ‐1 gμ = 0.00077 mΩ‐1

## Slide 13: Transistor Model - BJT
Example: Given an npn transistor β = 40, IC = 2mA, VA = ‐ 65 volts
  gm = 80 mΩ‐1 gπ = 2 mΩ‐1
  go = 0.031 mΩ‐1 gμ = 0.00077 mΩ‐1

## Slide 14: Transistor Model - BJT
Low frequency hybrid-π model
Because of the relative sizes of the g‐parameters, we can simplify the above model to

## Slide 15: Transistor Model - BJT
The small‐signal model for the BJT, we have so far, is only partially complete. We need to augment the model to incorporate other parameters that relate to the physical structure and physics of operation of the device:
    extrinsic resistances
    parasitic capacitances
    charge‐storage capacitances
The complete hybrid-π is
Typically, Cπ ≈10‐20pF
Cμ is an order of magnitude smaller

## Slide 16: Transistor Model - BJT
BJT can be expressed as a two-port network with emitter as a common terminal for both input and output ports.
The h-parameter is often provided in data sheet by manufacturers
The h-parameters and g-parameters are related as follows

## Slide 17: Transistor Model - BJT

## Slide 18: BJT Amplifier – AC Analysis
The above model is the complete model with intrinsic and extrinsic capacitance and resistance. It can be further simplified depending the frequency range in which the amplifier is working.
In mid-band frequency range, the intrinsic capacitances are and have very high impedances ( Zc=1/jwC) because the capacitance values are in the order of pf. Therefore, they can be considered as open. ( note that ru is very large)

## Slide 19: BJT Amplifier – AC Analysis

## Slide 20: BJT Amplifier – AC Analysis
AC Equivalent Circuit
  Steps in finding AC equivalent circuit ( in mid-frequency range)
    Disable independent DC sources
      DC Voltage sources to ground (or short circuited)
      Open circuit - DC current sources
    Replace non-linear transistors with linear small signal model
    Short large capacitors (in µf range) and open small capacitors (in pf range)

## Slide 21: BJT Amplifier – AC Analysis
Example:
Step 1 and 3:
Step 2:

## Slide 22: BJT Amplifier – AC Analysis

## Slide 23: BJT Amplifier – AC Analysis
Calculate voltage gain ( Av= Vo/Vs)

## Slide 24: BJT Amplifier – AC Analysis
Calculate input impedance

## Slide 25: BJT Amplifier – AC Analysis
Calculate output impedance

## Slide 26: BJT Amplifier – DC Analysis
DC biasing analysis of BJT amplifiers (steps)
  Open circuited any capacitor and short circuited any inductor
  Calculate the base voltage(s) of the first transistor ( transistors in the first stage) and determine whether the base-emitter junctions are forward biased. If so, assume VBE is around 0.7V.
  Further assume that the transistors are in forward active region and apply the normal collector, emitter, and base currents relationships (IC,IE,and IB). That is, IC = βIB.
  Calculate collector and emitter voltages, and check if the assumption of forward active is acceptable. If so, the calculated voltages and currents are DC biasing points. Otherwise, the transistors are in saturation region, in which case VCE = 0.2V.

## Slide 27: Transistor Model - BJT
Example 1:

## Slide 28: Transistor Model - BJT
Example 1:

## Slide 29: Transistor Model - BJT
Example 2:

## Slide 30: Transistor Model - BJT
Example 2:

## Slide 31: Transistor Model - BJT
Example 3: Determine the voltages at all nodes assume β=100.

## Slide 32: Transistor Model - BJT
Example 2:

## Slide 33: Transistor Model - BJT
Example 4: Determine the voltages and currents in the amplifier assume β=100.

## Slide 34: Transistor Model - BJT
Example 2:

## Slide 35: BJT Amplifier – Current Mirror
Transistors can be used to construct constant‐current sources which can in turn be used to bias a number of amplifier circuits.
Since the transistors are matched and on the same chip, the stages will track each other even if there is a change in the temperature or even the power‐supply voltage.

## Slide 36: BJE Amplifier – Current Mirror

## Slide 37: BJT Amplifier – Current Mirror
Current sources or mirrors are designed to maintain IC at a constant value even when VCE changes.
The Norton‐equivalent circuit of a current source
ro ≡ output resistance of the source, which is the output resistance seen at the collector of Q2.

## Slide 38: BJT Amplifier – Current Mirror
Now, it can be shown that the collector current is exponentially dependent on the base‐emitter voltage VBE :
where
  IS ≡ the saturation current of the transistor, which depends on the doping concentration and mobility of minority carriers in the base.
Since both transistors in a current source are fabricated on the same wafer, close to each other, the devices are well matched in β, VBE and IS, if they are of identical geometry.

## Slide 39: BJT Amplifier – Current Mirror
Taking KVL in the base loop
Hence,
Taking KVL in the CE loop of Q1

## Slide 40: BJT Amplifier – Current Mirror
For ,
VCC & R set the value IC1 and connection to Q1 mirrors IC1 onto IC2.
If the effect of the Early Voltage (VA) is included, then we must write:

## Slide 41: BJT Amplifier – Current Mirror
The output resistance of this simple current source is approximately given by

## Slide 42: BJT Amplifier – Current Mirror
Example:

## Slide 43: BJT Amplifier – Current Mirror

## Slide 44: BJT Amplifier – Current Mirror