## Slide 1: WEEK 4 Transistor Model - MOSFET
Dr. Aron Michael 2023
Electrical Engineering & Telecommunications
Engineering

## Slide 3: Learning Outcomes
At the end of this week, you will be able to
  Draw the small signal circuit model of MOSFET.
  Calculate the small signal circuit model parameters of MOSFET.
  Draw the small signal equivalent circuit of MOSFET based amplifiers.
  Analyze the performance of the amplifiers such as gain, bandwidth, input impedance and output impedance.
  Draw the DC equivalent circuit of MOSFET based amplifiers and calculate the quiescent values (IDQ, ISQ, VDSQ ).
  Explain DC biasing configurations such as current mirrors.

## Slide 4: Transistor Circuit Model - MOSFET
Linearization and graphical analysis
  Concerned with small signal variations about the operating points.
  Interested in a relationship between id, vgs and vds

## Slide 5: Transistor Circuit Model - MOSFET

## Slide 6: Transistor Circuit Model - MOSFET
Linearization and graphical analysis
  The voltage‐controlled current source gmvgs relates id to vgs for the MOSFET operating in the saturation region. gm is given by the slope of the transfer characteristic at the operating point

## Slide 7: Transistor Circuit Model - MOSFET
Calculation of gm and ro
(A/V2)
Process transconductance parameter for n-channel MOSFET
(m2/Vs)
Electron mobility
)
Gate oxide capacitance per unit area

## Slide 8: Transistor Circuit Model - MOSFET
Note:
  gm depends on aspect ratio
  gm depends on bias pt.
  Typically,
For ID= 1mA, = 1 gm = 0.2mA/V
= 10 gm = 0.632mA/V
Compare to BJT at 1mA, gm = 38.4mA/V

## Slide 9: Transistor Circuit Model - MOSFET
In spite of its low gm, MOSFET have other advantages: high Zin, small size, low power dissipation & ease of fabrication.
Note:‐ gm of BJT is geometry independent.
ro ≡ output resistance ⎯ slope of the output characteristic evaluated at the operating point ⎯ due to channel length modulation:
Evaluated at the operating point
typically ro ranges from 10k→100kΩ.

## Slide 10: Transistor Circuit Model - MOSFET
The low frequency model can be modified to include intrinsic capacitors and resistors to obtain high frequency model
Range: fraction of pF to 1 or 2 pF, depending on device size.
Note: Cgd contributes significantly to the Miller effect, resulting in reduction of gain at high frequencies ⎯ (covered later in the course).
Cgs ≡ gate‐source capacitance Cgd ≡ gate‐drain capacitance
Cds ≡ drain – substrate capacitance

## Slide 11: Transistor Circuit Model - MOSFET
Example 1: Common Source Amplifier

## Slide 12: Transistor Circuit Model - MOSFET
Calculate voltage gain ( Av = Vo/Vs)

## Slide 13: Transistor Circuit Model - MOSFET
Calculate input impedance (Rin)

## Slide 14: Transistor Circuit Model - MOSFET
Output impedance (Rout)

## Slide 15: Transistor Circuit Model - MOSFET
DC analysis of MOSFET circuits requires the following relations
  For n-MOS
      saturation region VGS >VT and VDS >VGS-VT
      triode (ohmic) region VGS>VT and
      0<VDS<VGS-VT
    cut off region VGS <VT, VDS ≤ VT

## Slide 16: Transistor Circuit Model - MOSFET
DC analysis of MOSFET circuits requires the following relations
  For p-MOS
  saturation region VGS <VT and
  VDS <VGS
  triode (ohmic) region VGS<VT
  and 0>VDS>VGS-VT
    cut off region VGS > VT , VDS ≤ VT
-
-

## Slide 17: Transistor Circuit Model - MOSFET
Steps in DC analysis
  Open circuit all capacitors (coupling capacitors) and short circuit all inductors if any
  Calculate gate voltage (VG) or gate-source voltage (VGS)
  Based on VG or VGS , guess possible operating region that the transistor can be. (Saturation, triode or cut off)
  Calculate DC biasing voltages and currents
  Check if your assumption in (d) is valid. If valid, then the calculated DC biasing voltages and currents are correct. Otherwise, repeat steps (d-f).

## Slide 18: Transistor Circuit Model - MOSFET
Example:
Where
Vt

## Slide 19: Transistor Circuit Model - MOSFET

## Slide 20: Transistor Circuit Model - MOSFET
Example 2:

## Slide 21: Transistor Circuit Model - MOSFET

## Slide 22: Transistor Circuit Model - MOSFET
  Using enhancement mode MOSFET (with threshold voltage (VT))
  Since VG = VD , the condition of VDS> VGS-VT is satisfied, and therefore the MOSFET is operating in saturation region

## Slide 23: Transistor Circuit Model - MOSFET
Simple current mirror (Q1 and Q2 in saturation)
Usually, is sufficiently small such that the Io: IREF is determined by the aspect ratio of W2/L2: W1/L1.This flexibility is at the disposal of the IC designer i.e. One can determine the desired current ratio by choosing the transistor sizes.
Again, the output resistance is given by:

## Slide 24: Transistor Circuit Model - MOSFET

## Slide 25: Transistor Circuit Model - MOSFET

## Slide 26: Transistor Circuit Model - MOSFET