## Slide 1: WEEK 5 Transistor Amplifiers – Frequency Response
Dr. Aron Michael 2023
Electrical Engineering & Telecommunications
Engineering

## Slide 3: Learning Outcomes
At the end of this week, you will be able to
  Explain and apply short and open circuit time constant methods.
  Calculate the lower and higher cut off frequencies of amplifier circuits.
  Explain and apply Miller Theorem and Miller’s effect in frequency analysis of amplifier circuits.
  Improve frequency response amplifiers by minimizing Miller’s effect.
  Calculate fT of BJT transistor and its relationship with parasitic capacitances.

## Slide 4: Short Circuit Time Constant
At low frequency, apply short circuit time constant method
  where is the jth pole of the gain function
  is short-circuit time constant associated with Cj
is the effective resistance seen by Cj when all Ci≠j
are short circuited and independent sources are
disabled.
Hence, the sum of the poles equals the sum of the reciprocals of the short-circuit time constants. Each of the terms ( ’s) is found for the specific capacitance in isolation, i.e, the other capacitances are short circuited.

## Slide 5: Short Circuit Time Constant
The dominant-pole approximation can be made if the highest-frequency pole is separated from the next pole or zero by at least two octaves (i.e., a factor of 4)
For LOW FREQUENCY analysis, if p1, is the dominant pole p1p2 (poles widely separated)
If the response is not dominated by a single pole, a good design procedure is to assume that the sum of poles is  1.15ωL

## Slide 6: Short Circuit Time Constant
The low frequency characteristics of an amplifier transfer function are due to the capacitances introduced into the circuit by the designer.
Example: Calculate the lower cut off frequency, fL

## Slide 7: Short Circuit Time Constant

## Slide 8: Short Circuit Time Constant
Draw the circuit as its small-signal equivalent
  Note that ru is neglected as it simplifies analysis
  Cπ and Cµ are neglected at low frequency
An estimate of fL can be obtained by calculating the short-circuit time constant associated with each capacitor

## Slide 9: Short Circuit Time Constant
Short circuit time constant associated with Cc1 with CE and Cc2 short circuited.
  Switch off the input voltage Vs

## Slide 10: Short Circuit Time Constant

## Slide 11: Short Circuit Time Constant

## Slide 12: Short Circuit Time Constant
Short circuit time constant due to CE with Cc1 and Cc2 short circuited
  The equivalent resistance seen by CE is found by analyzing the following

## Slide 13: Short Circuit Time Constant
Assuming ro has become infinite to simplify matters ( it has very little effect anyway). The circuit then becomes:

## Slide 14: Short Circuit Time Constant
Assuming ro has become infinite to simplify matters ( it has very little effect anyway). The circuit then becomes:

## Slide 15: Short Circuit Time Constant

## Slide 16: Short Circuit Time Constant
Short circuit constant due to Cc2 with Cc1 and CE short-circuited.

## Slide 17: Short Circuit Time Constant
Calculating ωL
  We now have terms for each of the three capacitors. This means we can estimate the lower corner frequency for this circuit. Using the definition presented earlier, we have:
  We can design for a specific value for fL by choosing values for CE, Cc1 and Cc2.
  When designing a circuit we make use of the fact that R’E is the smallest resistance and select CE so that the term due to it is the dominant pole. In a typical design, CE is selected so that we have 1/CER’E=0.8ωL with the remaining 20% split evenly between the other two terms.

## Slide 18: Short Circuit Time Constant
Example 2

## Slide 19: Short Circuit Time Constant

## Slide 20: Short Circuit Time Constant

## Slide 21: Short Circuit Time Constant

## Slide 22: Open Circuit Time Constant
For High-Frequency amplifier circuits
  Where is the jth pole of the gain function
  is open-circuit time constant associated with Cj
is the effective resistance seen by Cj when all Ci≠j are open
circuited and independent sources are disabled.
Hence, the sum of the reciprocals of the poles equals the sum of the open-circuit time constants. Each of the terms (τ’s) is found for the specific capacitance in isolation, i.e, the other capacitances are open circuited.

## Slide 23: Open Circuit Time Constant
For HIGH FREQUENCY analysis, if p1, is the dominant pole 1/p11/p2 then:
If the response is not dominated by a single pole, a good design procedure is to assume that the sum of poles is  1.15/ωH

## Slide 24: Miller’s Theorem
Consider an arbitrary circuit configuration of N distinct nodes where the node voltages are with reference to VN = 0 – ground.
Consider nodes 1 and 2 with an impedance Z connected between them. We postulate that the voltage ratio (i.e., gain) between nodes 1 and 2 is

## Slide 25: Miller’s Theorem

## Slide 26: Miller’s Theorem
This means that the current drawn from node 1, (i.e., I1 ) can be obtained by disconnecting Z from node 1 and placing an impedance Z1 between node 1 and VN, i.e., ground.
Proceeding in a similar manner for I2, we find the following:

## Slide 27: Miller’s Theorem
We can now replace the original circuit by the following
Miller equivalent circuit is valid only as long as K is unchanged. For example, the Miller equivalent circuit can not be used directly to determine output resistance and reverse transmission of the amplifier.
In practice, it is difficult to determine K independently and often the feed-through effects between input and output are neglected. For this reason, the transfer function obtained from the exact analysis differs slightly from that of the miller transformed circuit.

## Slide 28: Miller’s Theorem
We can now replace the original circuit by the following
Miller equivalent circuit is valid only as long as K is unchanged. For example, the Miller equivalent circuit can not be used directly to determine output resistance and reverse transmission of the amplifier.
In practice, it is difficult to determine K independently and often the feed-through effects between input and output are neglected. For this reason, the transfer function obtained from the exact analysis differs slightly from that of the miller transformed circuit.

## Slide 29: Miller’s Theorem

## Slide 30: High Frequency Analysis
Example: CE amplifier – Calculate fH

## Slide 31: High Frequency Analysis
AC equivalent circuit

## Slide 32: High Frequency Analysis
Calculate time constants

## Slide 33: High Frequency Analysis
  MILLER EFFECT
    The small capacitance Cµ due to amplification gives rise to a substantial capacitance between the base and ground. The large capacitance will actually limit the high-frequency response of the circuit. This multiplication of the effective value of the capacitance Cµ is known as MILLER EFFECT.
    The Miller Effect will be the determining factor for high-frequency response in circuits that experience it and severely affect the high-frequency response.
    How do we then get high gain from a circuit while minimising or even avoiding the Miller effect?

## Slide 34: High Frequency Analysis
  Miller Effect
  Recall that the corner frequency, ωH , is determined by two things, namely:
    Cµ multiplication ( the Miller effect) – signal feed through- observe that Cµ is multiplied by (1 + |gain|). For the CE case, this gain is  |gmR’L|.
    The resistance ‘seen’ by the capacitor ( 1+ |gain|)Cµ.
  To improve on ωH, we need to modify one of the terms or preferably both.

## Slide 35: High Frequency Analysis
  Improving frequency response
  Common base amplifier

## Slide 36: High Frequency Analysis
  Improving frequency response
  Common base amplifier
  The most important aspect of this circuit is that there is no feedback capacitor as for the common-emitter circuit. This means that there is no Miller effect and we would expect the higher corner frequency for the common-base circuit to be larger than that for a common-emitter circuit.

## Slide 37: High Frequency Analysis
  Improving frequency response
  Cascode configuration - frequency response can be improved by reducing the |gain| term in Millers Effect by ensuring R’L is low. This can be achieved by driving into the emitter of a common-base configuration.

## Slide 38: High Frequency Analysis
  Improving frequency response
  Cascode configuration – explanation
  The common-emitter stage sees the common-base stage as its load. This load is equal to the input resistance of the common base stage, which is equal to re – typically 25Ω, i.e., very low. This reduces the Miller effect since RL has been reduced. Since the collector current through Q2 is approximately equal to that of Q1, the mid-band gain doesn’t suffer. Another way to think of it is that Q2 is acting like a current buffer that passes on the current signal to the load while presenting a low load resistance to the amplifying transistor Q1

## Slide 39: High Frequency Analysis
  Improving frequency response
  Long tail pair: CC – CB

## Slide 40: High Frequency Analysis
  Improving frequency response
  Explanation
  CC has low voltage gain. Hence, it does not exhibit Miller effect. But provides current gain.
  CB provides voltage gain. However, there is no capacitor between emitter and collector. Hence, no Miller’s effect can be observed.

## Slide 41: High Frequency Analysis
  Improving frequency response
  CC – CE

## Slide 42: High Frequency Analysis
  Improving frequency response
  CC – CE
  Explanation
  Output resistance of CC stage is very low – looks like a signal source with very low output resistance. The CC stage does not suffer from the Miler effect.
  The voltage gain provided by the CE stage, which does suffer from the Millers effect. However, the multiplied capacitance of the CE stage “sees” a much smaller resistance due to the CC stage. Hence, it has lower open circuit time constant and therefore larger high corner frequency

## Slide 43: High Frequency Analysis

## Slide 44: High Frequency Limit – Hybrid-π Model
  Consider a BJT operating at high frequency. The minority carriers in the base need time to diffuse from the emitter to the collector: the base transit time, τt.
  The hybrid-π model will work well for the case of τt 1/f , where f is the frequency of the input signal.
  A figure of merit is that we should have f such that f ≤ (1/3)fT to ensure the hybrid-π model works well.
  fT is defined as the frequency at which the short-circuit current gain (β=hfe) of the transistor is unity.

## Slide 45: High Frequency Limit – Hybrid-π Model

## Slide 46: High Frequency Limit – Hybrid-π Model

## Slide 47: High Frequency Limit – Hybrid-π Model

## Slide 48: High Frequency Limit – Hybrid-π Model

## Slide 49: High Frequency Limit – Hybrid-π Model
Example: βdc=100; Cπ = 20pF ; Cµ = 2pF; IC= 0.25mA
Calculate fβ and fT

## Slide 50: High Frequency Analysis
Example

## Slide 51: High Frequency Analysis

## Slide 52: High Frequency Analysis
Example 2:

## Slide 53: High Frequency Analysis

## Slide 54: High Frequency Analysis